## Slide 1: Solvent-less Water based Inks for Non Porous Substrates
Igor Belošić, MBA, M. Eng.
Matjaž Mramor, DFTA

## Slide 2: Today
However…
DECADES OF INNOVATION
Solvent Based Inks serve us well
Now with “universal” products
Provide a full range of possibilities
Cost effective
Solvents are a non-renewable resource
They present a management control burden and – even if small – a risk

## Slide 3: In Future
The alternatives must meet market demands for:
Technical performance (physical)
Productivity (speed / down time for cleaning)
Total cost of ownership
Quality of graphics

## Slide 4: Your choices
Offset options
Flexo/ gravure options
Water- based inks
Water-based Electron Beam (EB) cured inks
Wetflex
Conventional UV flexo inks
Electron Beam (EB) cured inks
Conventional UV cured inks

## Slide 5
Water- based inks
Water-based Electron Beam (EB) cured inks
Wetflex
Electron Beam (EB) cured inks
Water-based Electron Beam (EB) cured inks
Water- based inks
Electron Beam (EB) cured inks
Wetflex
The Menu…

## Slide 6: Overall Statement Europe
a
The total use of inks and coatings in the European flexible packaging industry is estimated to ~200,000 tons per year
Less than 10,000 tons are WB (~5%)
Full conversion of plants to WB inks has only been done in the PE converting industry (for garbage and mailing bags for instance)
No major generalist converters have fully migrated to WB
  WB inks are less polyvalent than SB
  Negative impact on press speed, especially with backing white
  Regulations have not reached a point where SB are no longer suitable

## Slide 7: Applications Space Water Based Inks for flexible packaging

## Slide 8
Carrier bags
Magazine wrap
In-line extruded PE bags
Cups, plates
Non-woven
OK Compost bags
Shrink sleeves
Laminated food pouches
Deep freeze pouches
Butter packaging
Garbage bags
Diapers, towels wrap
Food, snack pouches
Adhesive tapes
Outdoor bags, pallet hood
PE
Foil
Other films
Metallised gift wrap

## Slide 9: Applications space – examples
Reverse on PE
Lamination PET/PE
Reverse on Sleeves
OK Compost
Direct print on PVDC
Direct on board/PE or board/PP
Direct print on PE, PP & PET

## Slide 10: What Does Each Technology Offer?
Water-based Electron Beam (EB) cured inks
Water- based inks
Electron Beam (EB) cured inks
Wetflex
Water-based Electron Beam (EB) cured inks
Electron Beam (EB) cured inks
Wetflex
Water- based inks
Water- based Inks
A cost effective option
Can be printed on existing presses
Boost air flow for higher speeds
Suitable for Flexo and Gravure
Suited to lamination
Excellent for process printing
HD also an option
Resistant surface print options available(after polimerisation like „glass” on surface-excellent adhesion, scratch resistance, fett resistance, water resistance)

## Slide 11: Summary
Water-based flexo / gravure inks are a good low cost option for lamination and can be printed on existing presses
Electron Beam water-based versions are required for surface print with good resolubility
WetFlex specifically offers gravure quality high speed printing and is an “Ultra Press friendly” solution
Electron Beam Offset is the best option for fast turnaround / short run with low cost plates based on the extended gamut concept

## Slide 12: Shift of ink material structure and cost
20-30% lower consumption of whites and overprint varnish
  Finer anilox rollers with WB for lower transfer/cost effective
Stronger coloured bases
  +100% TV in finished inks)
No need of let-down solvent (~30% of SB ink volume)
  Replace by ~5% of let-down water
No need of “viscosity” solvent
Coloured base
Technology varnish
Solvent
Coloured base
Technology varnish
Water
SB
WB
Notes: SB boja – puno pigmenta radi loseg transfera…
Nema podešavanje više viskoziteta … kod vodene – jedna briga manje! Čovjek manje..
Pigment WB nije RASTPOLJEN(DISOLVED) VEĆ JE DISPERGIRAN.
prednost toga je stabilnost otiska i boja se može puno jače pigmentirat.

## Slide 13: Fundamental difference between SB and WB inks: film-forming stage
Dispersed resin is insoluble in water at all pH
  There is in principle no resolubility of ink into itself once dispersed resins starts to coalesce (resin micelles fuse together)
  This fundamental effect drives every aspect of printing WB inks
Film forming mechanism of WB inks: coalescence
  Entirely new mechanism / solvent-based
  Coalescence is slow: full properties take 48-72 hrs to develop
  Sun Chemical inks generally have key advantage with properties at t=0
Drying
Coalescence
Acrylic dispersion in water
Stage 1
Water evaporates, particles get into close contact, start to pack
Stage 2
Particles deform
Particles are packing
Stage 3
Coalescence, polymer chains entangle and particle boundaries disappear

## Slide 14: Cost matters
Accurate cost-in-use comparison is not easily available
WB inks are 20-35% more cost efficient than SB inks (inks + solvent)
  Approx -20% for large plants using ~250 tons of inks per annum
  Approx -25% for small plants using ~40 tons of inks per annum
Main differences are
  WB inks require more energy for drying (no auto feed from solvent) – but no incineration!
  WB inks have higher waste treatment cost
  WB inks are cheaper per m²

## Slide 15: A project that impacts the whole company
Investments Running costs
Productivity
Impact on sales
Rules
Quality
Performance
Health / safety
Workers motivation
Image
Business
Technical
Human

## Slide 16: First of all, moving to WB means…
Facing resistance to changing work habits.
Requires:
  Strong leadership
  Motivation

## Slide 17: And then, moving to WB means…
A source of frustration.
Requires:
  Clear and shared objectives
  A clear roadmap
  Anticipated road-blocks

## Slide 18: Conclusions
WB inks are mature enough to address most challenges
Newest presses are well designed to run WB but some older presses can be retro-fitted without excessive costs. Speed will be limited by drying
Corona treatment is mandatory (no exceptions)
Sun Chemical have vast and deeply rooted expertise

## Slide 19: Sun Chemical’s Technology concept
SunSpectro Aqua and SunStrato Aqua are Sun Chemical’s product families of WB inks for films and foil
A single Coloured base range + bespoke technology varnishes
Dedicated portfolio of finished products:
  AquaLam Laminated structures
  AquaThene Polyethylene applications and Biodegradable films (carrier, outdoor, deep freeze, shrink wraps, garbage…)
  AquaFoil Aluminium foil
  AquaSleeve Shrink sleeves
  AquaProp Non-Woven, salad and snack pouches
  AquaTape Adhesive tapes

## Slide 20: THANK YOU! igor.belosic@sunchemical.com